## Slide 1
Wireless Networking
Lecture 1
Introduction to Wireless Networking

## Slide 2: References
Schiller, J.H. (2003), Mobile Communications, Second Chapter 1: Introduction
Price, R. (2006), Fundamentals of Wireless Networking. Chapter 1: Introduction to Wireless Networks

## Slide 3: Future Computing Devices
Computers are integrated (small, cheap, portable, replaceable - no more separate devices)
Computer are aware of their environment and adapt (“location awareness”)
Computer recognise the location of the user and react appropriately (e.g., call forwarding, fax forwarding, “context awareness”))

## Slide 4: Technological Advances
Advances in technology
  more computing power in smaller devices
  flat, lightweight displays with low power consumption
  new user interfaces due to small dimensions
  more bandwidth
  multiple wireless interfaces: wireless LANs, wireless WANs, regional wireless telecommunication networks etc.

## Slide 5: Mobility
Two aspects of mobility:
  user mobility: users communicate (wireless) “anytime, anywhere, with anyone”
  device portability: devices can be connected anytime, anywhere to the network

## Slide 6: Integration of Wireless Networks
Wireless vs. Mobile Examples   stationary computer   notebook in a hotel   wireless LANs in historic buildings   Personal Digital Assistant (PDA)
The demand for mobile communication creates the need for integration of wireless networks into existing fixed networks:
  local area networks: standardisation of IEEE 802.11
  Internet: Mobile IP extension of the internet protocol IP
  wide area networks: e.g., internetworking of GSM and ISDN, VoIP over WLAN and POTS

## Slide 7: Applications
Vehicles
  transmission of news, road condition, weather, music via DAB/DVB-T
  personal communication using GSM/UMTS
  position via GPS
  local ad-hoc network with vehicles close-by to prevent accidents, guidance system, redundancy
  vehicle data (e.g., from buses, high-speed trains) can be transmitted in advance for maintenance

## Slide 8: Applications
Emergencies
  early transmission of patient data to the hospital, current status, first diagnosis
  replacement of a fixed infrastructure in case of earthquakes, hurricanes, fire etc.
  crisis, war, ...

## Slide 9: Typical Application: Road traffic
ad hoc
UMTS, WLAN,
DAB, DVB, GSM,
cdma2000, TETRA, ...
Personal Travel Assistant,
PDA, Laptop,
GSM, UMTS, WLAN,
Bluetooth, ...

## Slide 10: Mobile and Wireless Services
UMTS
2 Mbit/s
UMTS, GSM
384 kbit/s
LAN
100 Mbit/s,
WLAN
54 Mbit/s
UMTS, GSM
115 kbit/s
GSM 115 kbit/s,
WLAN 11 Mbit/s
GSM/GPRS 53 kbit/s
Bluetooth 500 kbit/s
GSM/EDGE 384 kbit/s,
DSL/WLAN 3 Mbit/s
DSL/ WLAN
3 Mbit/s

## Slide 11: More Applications
Travelling salesmen
  direct access to customer files stored in a central location
  consistent databases for all agents
  mobile office
Replacement of fixed networks
  remote sensors, e.g., weather, earth activities
  flexibility for trade shows
  LANs in historic buildings
Entertainment, education, ...
  outdoor Internet access
  intelligent travel guide with up-to-date location dependent information
  ad-hoc networks for multi user games
History
Info

## Slide 12: Location dependent services
Location aware services
  what services, e.g., printer, fax, phone, server etc. exist in the local environment
Follow-on services
  automatic call-forwarding, transmission of the actual workspace to the current location
Information services
  “push”: e.g., current special offers in the supermarket
  “pull”: e.g., where is the Black Forrest Cheese Cake?
Support services
  caches, intermediate results, state information etc. “follow” the mobile device through the fixed network
Privacy
  who should gain knowledge about the location

## Slide 13: Mobile devices
performance
Pager
receive only
tiny displays
simple text messages
Mobile phones
voice, data
simple graphical displays
PDA
graphical displays
character recognition
simplified WWW
Smartphone
tiny keyboard
simple versions of standard applications
Laptop/Notebook
fully functional
standard applications
Sensors,
embedded
controllers
www.scatterweb.net
No clear separation between device types possible
(e.g. smart phones, embedded PCs, …)

## Slide 14: Effects of device portability
Power consumption
  limited computing power, low quality displays, small disks due to limited battery capacity
Loss of data
  higher probability, has to be included in advance into the design (e.g., defects, theft)
Limited user interfaces
  compromise between size of fingers and portability
  integration of character/voice recognition, abstract symbols
Limited memory
  limited usage of mass memories with moving parts
  flash-memory or ? as alternative

## Slide 15: Wireless networks in comparison to fixed networks
Higher loss-rates due to interference
  emissions of, e.g., engines, lightning
Restrictive regulations of frequencies
  frequencies have to be coordinated, useful frequencies are almost all occupied
Low transmission rates
  local some Mbit/s, regional currently, e.g., 53kbit/s with GSM/GPRS or about 150 kbit/s using EDGE
Higher delays, higher jitter
  connection setup time with GSM in the second range, several hundred milliseconds for other wireless systems
Lower security, simpler active attacking
  radio interface accessible for everyone, base station can be simulated, thus attracting calls from mobile phones
Always shared medium
  secure access mechanisms important

## Slide 16: Early history of wireless communication
Many people in history used light for communication
  heliographs, flags (“semaphore”), ...
  150 BC smoke signals for communication; (Polybius, Greece)
  1794, optical telegraph, Claude Chappe
Here electromagnetic waves are of special importance:
  1831 Faraday demonstrates electromagnetic induction
  J. Maxwell (1831-79): theory of electromagnetic fields, wave equations (1864)
  H. Hertz (1857-94): demonstrates with an experiment the wave character of electrical transmission through space (1888, in Karlsruhe, Germany)

## Slide 17: History of wireless communication I
1896 Guglielmo Marconi
  first demonstration of wireless telegraphy (digital!)
  long wave transmission, high transmission power necessary (> 200kW)
1907 Commercial transatlantic connections
  huge base stations (30 100m high antennas)
1915 Wireless voice transmission New York - San Francisco
1920 Discovery of short waves by Marconi
  reflection at the ionosphere
  smaller sender and receiver, possible due to the invention of the vacuum tube (1906, Lee DeForest and Robert von Lieben)
1926 Train-phone on the line Hamburg - Berlin
  wires parallel to the railroad track

## Slide 18: History of wireless communication II
1928 many TV broadcast trials (across Atlantic, color TV, news)
1933 Frequency modulation (E. H. Armstrong)
1950’s Analog, connection setup only from the mobile station, no handover
  1970’s analog, connection setup from the fixed network too (but location of the mobile station has to be known)
1982 Start of GSM-specification
  goal: pan-European digital mobile phone system with roaming
1983 Start of the American AMPS (Advanced Mobile Phone System, analog)
1984 CT-1 standard (Europe) for cordless telephones

## Slide 19: History of wireless communication III
1991 Specification of DECT
  Digital European Cordless Telephone (today: Digital Enhanced Cordless Telecommunications)
  1880-1900MHz, ~100-500m range, 120 duplex channels, 1.2Mbit/s data transmission, voice encryption, authentication, up to several 10000 user/km2, used in more than 50 countries
1992 Start of GSM roll-out
  fully digital, 900MHz, 124 channels
  automatic location, hand-over, cellular
  roaming in Europe - now worldwide in more than 200 countries
  services: data with 9.6kbit/s, FAX, voice, ...

## Slide 20: History of wireless communication IV
1996 HiperLAN (High Performance Radio Local Area Network)
  ETSI, standardisation of type 1: 5.15 - 5.30GHz, 23.5Mbit/s
  recommendations for type 2 and 3 (both 5GHz) and 4 (17GHz) as wireless ATM-networks (up to 155Mbit/s)
1997 Wireless LAN - IEEE802.11
  IEEE standard, 2.4 - 2.5GHz and infrared, 2Mbit/s
  already many (proprietary) products available in the beginning
1998 Specification of GSM successors
  for UMTS (Universal Mobile Telecommunications System) as European proposals for IMT-2000
  Iridium
    66 satellites (+6 spare), 1.6GHz to the mobile phone

## Slide 21: History of wireless communication V
1999 Standardization of additional wireless LANs
  IEEE standard 802.11b, 2.4-2.5GHz, 11Mbit/s
  Bluetooth for piconets, 2.4GHz, <1Mbit/s
  decision about IMT-2000
    several “members” of a “family”: UMTS, cdma2000, DECT, …
  Start of WAP (Wireless Application Protocol) and i-mode
    first step towards a unified Internet/mobile communication system
    access to many services via the mobile phone
2000 GSM with higher data rates
  first GPRS trials with up to 50 kbit/s (packet oriented!)
  UMTS auctions/beauty contests
    Hype followed by disillusionment (50 B$ paid in Germany for 6 licenses!)
  Iridium goes bankrupt
2001 Start of 3G systems
  Cdma2000 in Korea, UMTS tests in Europe, Foma (almost UMTS) in Japan

## Slide 22: History of wireless communication VI
2002
  WLAN hot-spots start to spread
2003
  UMTS starts
  Start of DVB-T replacing analog TV
2005
  WiMax starts as DSL alternative (not mobile)
  first ZigBee products
2006
  HSDPA starts as fast UMTS download version offering > 3 Mbit/s
  WLAN draft for 250 Mbit/s (802.11n) using MIMO
  WPA2 mandatory for Wi-Fi WLAN devices
2007
  over 3.3 billion subscribers for mobile phones (NOT 3 bn people!)
2008
  “real” Internet widely available on mobile phones (standard browsers, decent data rates)
  7.2 Mbit/s HSDPA, 1.4 Mbit/s HSUPA available in Germany, more than 100 operators support HSPA worldwide, first LTE tests (>100 Mbit/s)
2009 – the story continues with netbooks, iphones, VoIPoWLAN…

## Slide 23: Mobile Subscriptions Worldwide

## Slide 24: Mobile Subscriptions (Ireland)

## Slide 25: Overlay Networks - the global goal
regional
metropolitan area
campus-based
in-house
vertical
handover
horizontal
handover
integration of heterogeneous fixed and mobile networks with varying transmission characteristics

## Slide 26: Areas of research in mobile communication
Wireless Communication
  transmission quality (bandwidth, error rate, delay)
  modulation, coding, interference
  media access, regulations
  ...
Mobility
  location dependent services
  location transparency
  quality of service support (delay, jitter, security)
  ...
Portability
  power consumption
  limited computing power, sizes of display, ...
  usability
  ...

## Slide 27: Reference Model
Application
Transport
Network
Data Link
Physical
Medium
Data Link
Physical
Application
Transport
Network
Data Link
Physical
Data Link
Physical
Network
Network
Radio

## Slide 28: Functions of Layers
Application layer
Transport layer
Network layer
Data link layer
Physical layer
service location
new/adaptive applications
multimedia
congestion/flow control
quality of service
addressing, routing
device location
hand-over
authentication
media access/control
multiplexing
encryption
modulation
interference
attenuation
frequency